## Slide 1
Use of observations by the Copernicus Atmosphere Monitoring Service for data assimilation and product evaluation over Europe
IWAQFR, Toronto, 11th January 2017
Plu, M.1, S. Guidotti1, J. Arteta1, M. Joly1, J. Parmentier1, L. Rouïl2, F. Meleux2, R. Engelen3, V.-H. Peuch3, A. M. Benedictow4, J. Douros5, H. Elbern6, H. Eskes5, E. Friese6, M. Gauss4, L. Robertson7, A. Segers8, M. Sofiev9, A. Valdebenito4
1: Meteo-France, France ; 2: INERIS, France ; 3: ECMWF, United Kingdom ; 4: MET Norway, Norway ; 5: KNMI, the Netherlands ; 6: RIU, Germany ; 7: SMHI, Sweden ; 8: TNO, the Netherlands ; 9: FMI, Finland.

## Slide 2: Plan
The Regional CAMS over Europe
Surface observations for CAMS over Europe
CAMS assimilation over Europe
Conclusion and perspectives

## Slide 3: The Regional CAMS over Europe
(see M. Pithon’s presentation yesterday)
Daily production
of air quality
forecasts and
Analyses (7 models & Ensemble)
Global model products
Regional emissions
Observations
Annual production of
air quality reanalyses
Interim (YY-1) & Validated (YY-2)
USERS
CHIMERE (INERIS)
EMEP (MET Norway)
EURAD-IM (RIUUK)
LOTOS-EUROS (KNMI/TNO)
MATCH (SMHI)
SILAM (FMI)
MOCAGE (Meteo-France)
AQUM (Met Office)
DEHM (Aarhus Univ.)
GEM-AQ (Warsaw Univ.)
7 operational models
3 models under development

## Slide 4: Surface observations for CAMS over Europe
How are surface observations used?
Monitoring
Filtering
Verification
of regional CAMS products
(NRT forecasts, analyses,
re-analyses)
Surface observations from EIONET
- « Near-Real time » (NRT) dataflow
- A posteriori validated dataflow
Data assimilation
in regional models
(NRT analyses,
re-analyses)
Ozone
NO2
SO2
CO
PM10
PM2.5

## Slide 5: Surface observations for CAMS over Europe
Selection of stations: use of an objective, homogeneous, and pollutant-specific classification (Joly and Peuch, 2012, Atmos. Env.):
  Based on the past hourly time series only,
  For each station and pollutant, 8 indicators are defined that cover the main features of the measured pollutant behaviour (diurnal cycle, week-end effect, winter/summer ratios...),
  Classification relies on a Linear Discriminant Analysis,
   10 classes are defined, and the stations classified as 1-5 are kept (background) for assimilation and evaluation in CAMS-Regional.

## Slide 6: Surface observations for CAMS over Europe
Cross-validation with meta-data (Joly and Peuch, 2012):
T: Traffic – U: Urban – S: Suburban – R: Rural
Notes: Correspondance between station type and class.
Higher correspondance for NO2 than for ozone

## Slide 7: Surface observations for CAMS over Europe
Ozone: Cross-validation with meta-data (Joly and Peuch, 2012)
T: Traffic – U: Urban – S: Suburban – R: Rural
Notes: Northern part of France, Germany, Poland: some U sites are now classified as bkground.
Suggests that the classification acts as a re-calibration.

## Slide 8: Surface observations for CAMS over Europe
The classification that is used in CAMS-Regional is being revised in order to:
  Update with regards to the surface measurements available (2014),
  Classify the stations for all the pollutants evaluated in CAMS-Regional: O3, NO2, PM10, PM2.5, SO2, CO (in test),
  Investigate some refinements of the method:
    Indicators: improvement of the definition/computation, addition of 6 new indicators, transformation of asymmetric distributions using a Box-Cox procedure, refinement of the detection of outliers (using a learning method),
    A Principal Component Analysis is now used,
    The LDA is multiple in order to separate the 4 groups of stations,
    New procedure to affect each station in its class.

## Slide 9: Plan
The Regional CAMS over Europe
Surface observations for CAMS over Europe
CAMS assimilation over Europe
Conclusion and perspectives

## Slide 10: CAMS assimilation over Europe
Assimilation systems
  Each of the 7 operational models have their own assimilation system, that can at least assimilate in-situ surface observations,
  Developments are on-going to assimilate more species and also to assimilate upper-level observations (satellite, profilers, etc),
  ~15% of the stations are kept for independent evaluation of the analyses,
  CAMS-Regional is a relevant test bed to evaluate:
    The added-value of assimilation with regards to free model forecasts,
    The benefit of satellite observations on surface analyses,
    The impact of assimilation on non-assimilated species,
    The impact of initializing forecasts by analyses.
  The 3 models “under development” will develop establish their assimilation system this year.

## Slide 11: CAMS assimilation over Europe
Assimilated species by each model (as of January 2017):
 | Method | O3 | NO2 | PM10 | PM2.5 | SO2 | CO
CHIMERE | O.I. | EEA | EEA | EEA | EEA | - | -
EMEP | 3D-VAR | EEA | EEA, OMI | - | - | EEA | -
EURAD-IM | 3D-VAR | EEA | EEA, OMI, GOME-2 | EEA | EEA | EEA | MOPITT
LOTOS-EUROS | EnKF | EEA | - | - | - | - | -
MATCH | 3D-VAR | EEA | EEA | EEA | EEA | EEA | EEA
MOCAGE | 3D-VAR | EEA | EEA | EEA | - | - | -
SILAM | 3D-VAR | EEA | EEA | - | EEA | - | -
Total assim. |  | 7 | 6 | 4 | 4 | 3 | 2
EEA: surface in-situ distributed by Meteo-France (NRT) or INERIS (reanalyses)
after retrieval from the EEA

## Slide 12: CAMS assimilation over Europe
How much better are the surface analyses compared to the surface forecasts?
RMSE of O3 analyses
RMSE of O3 forecasts

## Slide 13: CAMS assimilation over Europe
How much better are the surface analyses compared to the surface forecasts?
RMSE of PM10 analyses
RMSE of PM10 forecasts

## Slide 14: CAMS assimilation over Europe
On the impact of assimilation on non-assimilated species: effect of assimilating PM10 surface observations on PM2.5 with MOCAGE (Météo-France)
Parmentier, Arteta, Plu (CNRM, Météo-France/CNRS)

## Slide 15: CAMS assimilation over Europe
On the impact of assimilation on non-assimilated species: effect of assimilating PM10 surface observations on PM2.5 with MOCAGE
MOCAGE ASSIM PM10
MOCAGE FORECAST
ENSEMBLE
Parmentier, Arteta, Plu (CNRM, Météo-France/CNRS)
PM2.5 scores

## Slide 16: CAMS assimilation over Europe
On the impact of assimilation on non-assimilated species: effect of assimilating ozone surface observations on other species with LOTOS-EUROS (KNMI, TNO)
μg.m-3
Douros, Segers, Eskes (KNMI and TNO)
NO2 - Free run
NO2 – Assimilation O3
Difference

## Slide 17: CAMS assimilation over Europe
On the impact of assimilation on non-assimilated species: effect of assimilating ozone surface observations on other species with LOTOS-EUROS (KNMI, TNO)
Douros, Segers, Eskes (KNMI and TNO)
CO - Free run
CO2 – Assimilation O3
Difference
μg.m-3

## Slide 18: CAMS assimilation over Europe
On the benefit of assimilating upper-air observations for surface products: effect of assimilating MODIS AOD on PM surface analyses with EURAD-IM (RIUUK)
Without assimilation Assim MODIS_AOD
Assim MODIS_AOD+EEA_PM Reference observations
Averaged PM time-series for March 1st to 15th, 2013.
Friese, Elbern (RIUUK)
PM10
PM2.5
France
Germany

## Slide 19: CAMS assimilation over Europe
On the benefit of initializing forecasts by analyses: effect on ozone forecasts with EURAD_IM (RIUUK)
Ozone concentrations
at background AIRBASE
measurement sites
from 7th to 20th of July 2010.
Without assimilation
Initialized by analysis (every-24h)
Reference observations
France
Germany
Friese, Elbern (RIUUK)
(The analysis is the result of assimilation in EURAD-IM of surface and satellite observations)

## Slide 20: CAMS assimilation over Europe
On the benefit of initializing forecasts by analyses: effect on NO2 forecasts with EURAD_IM (RIUUK)
NO2 concentrations
at background AIRBASE
measurement sites
from 15th of January
to 3rd of February 2012.
France
Germany
Friese, Elbern (RIUUK)
(The analysis is the result of assimilation in EURAD-IM of surface and satellite observations)
Without assimilation
Initialized by analysis (every-24h)
Reference observations

## Slide 21: CAMS assimilation over Europe
On the benefit of initializing forecasts by analyses: effect on PM forecasts with EURAD_IM (RIUUK)
Friese, Elbern (RIUUK)
Without assimilation
Initialized by analysis
Reference observations
France
Germany
PM10 concentrations
at background AIRBASE
measurement sites
from 15th of January
to 3rd of February 2012.
(The analysis is the result of assimilation in EURAD-IM of surface and satellite observations)

## Slide 22: Conclusion
Surface observations are a key component of the CAMS Regional production over Europe, both for assimilation and for evaluation of the products,
Objective classification of surface stations is needed to select the most representative measurements for our purpose; revision and updates of the classification are on-going,
Results from the different models suggest (depending on the assimilation configuration, however):
  A positive impact of analyses on the successive forecasts of ozone, longer than for NO2 and for PM,
  Potential benefits of the assimilation of PM10 on PM2.5 analyses,
  Slight impact of the assimilation of ozone on other species,
  A benefit of the assimilation of MODIS AOD on PM surface analyses, as a complement of the assimilation of PM surface observations.

## Slide 23: Perspectives
Analyses at upper-levels will be developed from 2017,
3 new models (AQUM, DEHM, GEM-AQ) will develop and evaluate their own assimilation system in 2017,
The assimilation of upper-air observations is a mid-term perspective for many models: assimilation of aerosol profiles (lidars) and satellite optical depth (MODIS, Metop/PMAP, Sentinel-3, etc),
Potential for assimilation of reactive gases (ozone, NO2, SO2, HCHO, CHOCHO) over Europe from the upcoming Sentinels :
  Sentinel-5 (& -5P): polar-orbiting, UV-NIR-SWIR hyperspectral,
  Sentinel-4: geostationary (onboard METEOSAT 3rd Generation), UV-NIR hyperspectral.