## Slide 1: Development of an operational assimilation system utilizing a Regional Chemistry Transport Model of Japan Meteorological Agency
Masaaki Ikegami1,2, Akane Kamada1,2, Mizuo Kajino2, Makoto Deushi1,2
1Japan Meteorological Agency
2Meteorological Research Institute
Notes: Thank you, chairperson. I am Masaaki Ikegami with the Japan Meteorological Agency, JMA.
Today, I’d like to talk about recent improvement of the ozone chemistry transport model for photochemical oxidant prediction.

## Slide 2
Oxidant advisory
Category
advisory 2 (over 120 ppb)
advisory 1 (over 80 ppb)
advisory 0 (below 80 ppb)
Chemistry
Transport
Global CTM
(MRICCM2)
Photochemical oxidant advisory in Japan
Emission inventories
nesting
2015~
Regional CTM
(NHM-Chem)
Bias
correction
Deushi, 2011
Kajino, 2012
~110 km
20 km
O3
Global model analysis and forecast by JMA
JMA plan to adopt operationally the assimilation method in spring 2017.
Observed surface ozone concentrations
nudging
QC
Notes: First of all, I’ll show you some background. In Japan, photochemical oxidant has damaged our life since 1960s, and this risk has not gone away completely. This slide shows how we issue photochemical oxidant information to the public in Japan. At present we operationally use a global ozone chemistry transport model called MRI-CCM2 and regional CTM called NHM-Chem, to estimate surface ozone concentration for Japan. They ware developed by the Meteorological Research Institute (MRI) of JMA. According to the simulated oxidant concentration we diagnose an oxidant advisory of three categories to each prefecture. The categorization is like this, if daily maximum surface ozone concentration at each prefecture seemed to be over 120 ppb, it is categorized as level 2 and, we essentially provide information on photochemical oxidant. But the current model system not assimilate observed surface ozone concentrations. Therefore we developed a method to assimilate observed surface ozone concentrations using a nudging technique for the regional CTM. We are going to operate this in 2017.
（参考）
The MRI-CCM2 model (e.g. Shibata et al., 2005) is designed to simulate the distributions and time- evolutions of ozone and related chemical species over the troposphere and the middle atmosphere comprehensively, and used for the operational prediction of photochemical oxidant near the surface at the Japan Meteorological Agency. In the MRI-CCM2 model, a chemistry module is coupled with a general circulation model (GCM) via the MRI Scup coupler.

## Slide 3: Contents
Specification of prediction system
Observed data quality control
Data assimilation method (nudging)
Result of simulated Oxidant Verification
Notes: These are today’s topics.
First, I would like to introduce the surface ozone prediction system.
Next, I will talk about the observed data quality control.
Then I will present data assimilate method, and results of simulation.

## Slide 4
Global model analysis and forecast by JMA
Global CTM (MRI-CCM2)
nudging
Regional CTM (NHM-Chem)
JMANHM （20km）
Meteorological data
TL159L64
Horizontal 20km, 18 levels
1. Forecast system using regional - global CTM
Nesting
O3 NO2
NO CO
nudging
Emission inventories
Observed surface ozone concentrations
nudging
QC
4
Notes: Next slide shows the relation between the global CTM and the regional CTM. The global CTM use emission inventories and nudged toward the operational Global Numerical Weather Forecast model analysis and forecast by JMA. The global CTM simulates O3 (ozone), NO2 (nitric dioxide), NO (nitric oxide), CO (carbon monoxide) and other chemicals, so we nest them from the global model to the regional model. The regional CTM also uses emission inventories. As to meteorological data, it uses forecasts by JMANHM with 20km resolution. This meteorological model also uses global meteorological analysis as boundary condition. And this time, we are developed a method to assimilate observed surface ozone concentrations using a nudging technique to regional CTM.

## Slide 5
Specification of global CTM (Deushi and Shibata, 2011) |  |  | 
CTM Resolutions | TL159 (1.125°) / 64 levels (surface – 0.01 hPa) |  | 
Initial time and forecast time | At 12 UTC in 72 hours (once a day) |  | 
Tropospheric and Stratospheric Chemistry | Chemical species : 90 (long-lived: 64, short-lived: 26) |  | 
 | Chemical Reactions: 247 ( Photolytic: 59, Gas phase: 172, Heterogeneous: 16 ) |  | 
Emission inventories | EDGAR v2.0 | anthropogenic | Global
 | GEIA | natural | Global
 | REAS1.1 | anthropogenic | East Asia
Notes: Next slide is on the specification of our global CTM.
The model has a horizontal resolution of TL159 and 64 layers from surface up to 0.01 hPa. We operationally calculate the CTM once a day. The initial time is at 12 UTC, and forecast time has 72 hours.
The chemistry module has 90 chemical species, and 250 chemical reactions.
We use anthropogenic and natural emission inventories such as EDGAR, GEIA, and REAS. The REAS is East Asian anthropogenic emission inventory and is provided by Dr. Ohara in the National Institute for Environmental Study (NIES) in Japan.

## Slide 6
1. Specification of the regional CTM |  | 
Model Resolutions | 20 x 20 km ( Lambert Coordinates ) / 18 levels (surface – 50 hPa) | 
Meteorological /Chemical Module (off line coupled) | JMANHM(Meso-Scale Model by JMA) / RAQM2 (Kajino et al., 2012) | 
Tropospheric Gas Chemistry | Chemical species : 72 Chemical Reactions: 214 (SAPRC99; Carter, 2000) | 
Emission inventories | REAS1.1 | anthropogenic
 | MEGAN2, etc. | natural
 | GFED3 | biomass burning
Notes: This is specification about the regional CTM. Its horizontal resolution is 20 km by 20 km in Lambert Coordinates. The vertical resolution is 18 layers from the surface to 50 hPa in terrain-following coordinates. Its meteorological module is JMA’s meso-scale non-hydrostatic model. Its chemical module is RAQM2 developed by Dr. Kajino at MRI. We use the SAPRC99 gas-phase atmospheric chemical module and these emission inventories.

## Slide 7
2. Observed surface ozone concentrations Data quality control
no
yes
Oxt: Ox concentration at time t.
dOxt: deference of Ox concentration between time t and t-1.
mt(σt): mean (standard deviation) of Ox concentration at the nearest 6 ~ 10 stations from the station within its 50 km radius at time t.
QC5t: result (outlier or correct) of QC5 at time t.
winter: NOV. – FEB.
NA
Oxt<=250
(in winter: Oxt<= 100)
Oxt>=80
Oxt<=mt+5σt
|dOx|t<=90
Oxt=<mt+3σt
|dOx|t-1<=50 .and.
|dOx|t<=50
QC5t-1=outlier
outlier
outlier
outlier
correct
correct
correct
outlier
Oxt>=100
QC1
QC2
QC3
QC4
QC5
Notes: In japan, air quality is observed by local government. JMA can use near real-time observed surface ozone data; however, as to final result after data screening by local government (FINAL), JMA can use it about 2 years later.
Therefore we applied original quality control (QC) methods to near real-time data.
QC1 is gross check. It is rare for surface O3 concentration to increase over 250 ppb.
QC2 is spatial check. We previously calculated mean and standard deviation of O3 concentration at the nearest 6 ~ 10 stations from the station within its 50 km radius. If a value was within the mean plus minus 3sigma, it is identified correct.
QC3 is hourly difference check. If the deference of O3 concentration from previous value was within 50 ppb at time t and t-1, it is identified correct. QC4 has QC1, 2, 3. Moreover, QC5 is more strict spatial check and hourly different check if the data is over 100 ppb.

## Slide 8
 | Method | Ratio=(B+C)/total
 | near-real time data | 9.68%
QC1 | gross check | 6.64%
QC2 | spatial check | 8.32%
QC3 | hourly difference check | 6.65%
QC4 | combination of QC1, 2, 3 | 3.05%
QC5 | more strict check | 2.62%
 |  | FINAL | 
 |  | correct | outlier
QC5 | correct | 3889(A) | 48(B)
 | outlier | 68(C) | 418(D)
2. Observed surface ozone concentrations Data quality check
Notes: We compared near real-time data after these QC methods at 1191 stations from April 2010 to March 2013 with FINAL. 4423 samples were selected.
We classified outliers and others in every QC and FINAL as described in Table 5. Discrepancy rate of QC5 was best (Table 4). As result, we determined QC5 for data assimilation with NHM-Chem.

## Slide 9
Japan
2. interpolate observational data to regional model grid value
After the QC of the observations at each station, grid point values are calculated by averaging the observations in each model grid (20x20 km).
Notes: After the QC of the observations at each station, grid point values are calculated by averaging the observations in each model grid (20x20 km).

## Slide 10
05 JST
calculation end
Observed surface ozone concentrations
2200
0300 JST (local time)
Quality control
Interpolation to model grid
Regional CTM
（NHM-Chem）
Data assimilation by nudging
Forecast
2100
Global CTM
（MRI-CCM2）
2300
0200
・・・
・・・
Initial
・・・
・・・
・・・
72 hour (operational)
Boundary
3.Data assimilation system (nudging)
04JST (local time)
calculation start
Operational time schedule
Nudging in the boundary layer
Nudging time constant γ= 1/1000[s-1]
09:20 JST
Release the advisory
Notes: Our operational forecast system starts calculation at 04 japan standard time (JST) with initial time of 21 JST of the previous day.
Therefore, it assimilates oxidant data observed in 21 ~ 03 hours local time and forecasts after that.
We are perform observed ozone data assimilation by nudging in the boundary layer
Nudging time constant is 1000 seconds.

## Slide 11
4. Result
Observation
no assimilation
assimilation
Tokyo grid
Simulated concentrations of O3 are calculated continuously.
Observed O3 concentrations are assimilated only night time (21 ~ 03 local time) .
The regional model simulates diurnal variations very well.
Notes: To check the performance of this new assimilation method, we compered forecasts of the surface ozone concentration with observations. The period of the validation was from March to September 2015. This is an example of hourly observed values and simulated ones in August, 2015 at the regional CTM grid around Tokyo. Simulated concentrations of O3 are calculated continuously.
Observed O3 concentrations are assimilated only night time (21 ~ 03 local time) .
The regional model simulates diurnal variations very well. At night time, the model no assimilation tends to underestimate the ozone value. But the model surface ozone assimilated well reproduced those values during the assimilation on.

## Slide 12
4. Result
no assimilation
assimilation
21 0 3 6 9 12 15 18 21 JST (local time)
Tokyo grid
Hourly time series of mean error in August 2015 in Tokyo grid
Observed O3 concentrations are assimilated only night time (21 ~ 03 local time) .

## Slide 13
ozone assimilation | Mean Error | RMSE | R
OFF | 8.9 ppb | 15.7 ppb | 0.61
ON | 6.6 ppb | 13.7 ppb | 0.69
4. Result of simulated Oxidant Verification
We verified all the points with data in Japan area.
Verification term：March ~ September, 2015
Forecast period：04～20JST (local time)
Notes: We verified all the points with data in japan area. The verification is conducted during the period from march to September, 2015. The estimated model bias from the observation is reduced from 8.9 ppb to 6.6 ppb, RMSE is also reduced from 15.7 ppb to 13.7 ppb, and the correlation coefficient is improved from 0.61 to 0.69.

## Slide 14
Guidance
Observation daily maximum
Model
daily maximum
O3(ppb)
Guidance
=bias correction
O3(ppb)
frequency
(50%)
(35%)
(10%)
(5%)
67
78
85
(50%)
(35%)
(10%)
(5%)
<- category
Ⅰ
Ⅱ
Ⅲ
Ⅳ
80
100
120
Frequency Bias Correction Method
Ⅰ
Ⅱ
Ⅲ
Ⅳ
Ⅰ
Ⅱ
Ⅲ
Ⅳ
Statistical Guidance
We use this method to make statistic guidance at every prefecture and every month.
Notes: We forecast the daily maxima ozone concentrations by every prefecture. We make it from statistical guidance. So we conduct verification this statistical guidance too. First I explain the statistical guidance. Generally, model daily maxima ozone concentrations are lower than observed.
To compensate the underestimations of the daily maxima, a statistical guidance is introduced to our operational forecast system.
But before the statistical calculations, we have a problem that the frequency distribution of observation and model are different from each other. So, we need to correct the model frequency distribution.
Here, I divided observed daily maxima oxidant concentration into four categories at the thresholds by 80, 100, and 120 ppb.
The number of daily maximum oxidant concentrations is counted at each category. From this number frequency, we can newly calculate the appropriate threshold values in the model. These threshold values correspond to the categories of the model, and these model thresholds are used for the interpretation in the guidance.
If the simulated value is 82 ppb, the statistic guidance is 111 ppb. In this way we change simulated value to statistic guidance.

## Slide 15: Verification of statistical guidance Threat Score (TS) or Critical Success Index (CSI)
Its range is 0 to 1. Perfect forecast / TS=1
Obs. O3 assimilation | On | Off
TS | 0.33 | 0.32
120ppb Threat Score （2013-2016）
Yes
No
Yes
No
FO
FX
XO
XX
Event forecast
Event observed
O3 daily maximum
Since data assimilation is done only night time, it is not very effective for the daily maximum value.
Notes: To validate the statistic guidance, we use Threat Score (TS) or Critical Success Index (CSI) that is useful to validate rare phenomena. First, we categorize all the events into four by forecasted or not and observed or not like this table. Our target is rare phenomenon so XX number in this table is large. TS is the score without XX like this equation. Using this score, TS of the regional CTM assimilation on and off are 0.33 and 0.32.

## Slide 16: Summary
We are developing a method to assimilate observed surface ozone concentrations using a nudging technique.
The performance of model using the assimilation method is better than it did without using it.
We plan to adopt operationally the assimilation method in spring 2017.
Thank you for your attention!
Notes: In summary,
Thank you very much.

## Slide 17: Reference
Carter, W.: Documentation of the SAPRC-99 chemical mechanism for VOC reactivity assessment. Final report to California Air Resources Board, Rep. 92-329, Univ. of Calif., Riverside, 8 May, 2000.
Deushi, M. and Shibata, K.: Development of an MRI Chemistry-Climate Model ver.2 for the study of tropospheric and strarospheric chemistry, papers in Meteor. Geophys., 62, 1-46 (2011).
Kajino, M., Y. Inomata, K. Sato, H. Ueda, Z. Han, J. An, G. Katata, M. Deushi, T. Maki, N. Oshima, J. Kurokawa, T. Ohara, A. Takami, S. Hatakeyama: Development of an aerosol chemical transport model RAQM2 and prediction of Northeast Asian aerosol mass, size, chemistry, and the mixing type. Atmos. Chem. Phys., 12, 11833-11856, 2012