## Slide 1: Evolution of the Canadian Operational Air Quality Forecast Systems: Addressing Today’s Needs and Preparing for Tomorrow
IWAQFR 2017, Toronto, 2017.01.10
Didier Davignon1
With results/contributions from:
M.-D. Moran2, R. Pavlovic1, R. Munoz-Alpizar1, S. Menard1, H. Landry1, S. Gilbert1, P.-A. Beaulieu1, S. Cousineau1
1Air Quality Modeling Applications Section, Environment and Climate Change Canada,
Montreal, Quebec, Canada
2Air Quality Research Division, Environment and Climate Change Canada, Toronto, Ontario, Canada

## Slide 2: Summary
Description of current operational AQ systems
  Performance of systems (verification)
  Products and clients
Trends
Implications for future developments

## Slide 3: Context: Canada
Trend = air quality improving in general
  Attributed to NOx/SOx emission reductions, mostly due to
    Regulations in transportation
    Phasing out of coal-fired power plants in Canada and USA
  Fewer smog episodes reported
  Exception: summertime PM2.5, due to wildfire emissions
In large cities: similar observations
  Ozone trend not as clear: chemical regime shifting
Distribution of VOC to NOx ratios,
Simulated with AURAMS, 2006 vs 2020 projection (using total VOC for simplification)
Notes: Voc to Nox plots: as an indication only. Based on emission projections dating from 2011. Compiled all hours from an annual run produced with the AURAMS model at a 22.5km resolution.

## Slide 4
Annual (2010-2016) number of considered forecast & observed pairs
NO2
O3
PM2.5
OBSERVED
pollution trend
(2010-2016) for Canada
Decreasing trend
Slightly
decreasing trend
No clear trend
Hectares burned (1982-2016) by wildfires in Canada
Source: Canadian Interagency Forest Fire Centre
Strongly driven by wildfires

## Slide 5: Trend for ozone: seasonal
Source: Air Quality in Ontario 2014 Report

## Slide 6: Trends according to standards
Fine particulate matter and ground-level ozone air quality indicators relative to the 2015 Canadian Ambient Air Quality Standards, Canada, 2000 to 2014

## Slide 7
7-Year (2010-2016) Pollution Trends (Observed vs Forecasted ) in Montreal, Toronto and Vancouver
MONTREAL
TORONTO
VANCOUVER
NO2
O3
PM2.5
NO2
O3
PM2.5
NO2
O3
PM2.5
Forecasted
Observed
Forecasted
Observed
Forecasted
Observed

## Slide 8: MSC numerical modelling (partial overview)
Global deterministic
25km
240h, 2/d
Regional deterministic
10km, North America
48h/54h, 4/d (exp. 84h)
Global ensemble
50km, 20 members + cntrl
364h, 2/d ; 768h 1/w
Regional ensemble
15km, 20 members + cntrl
72h, 2/d
Global coupled:
Ocean, ice, waves…
Regional coupled:
Ocean, ice, waves Hydrology, …
Air quality (RAQDPS)
High resolution determ.
2.5km (National, North)
48h, 2/d
(Experimental)
High res. coupled:
(experimental / pilot)
High res surface model
Air quality …

## Slide 9: Regional Air Quality Deterministic Prediction System (RAQDPS): components
GEM-MACH coupled AQ & weather model
Operational environment and systems
Emissions:
- Anthropogenic - Biogenic
- (Forest fires)
AQ piloting from global model
Weather assimilation
Weather BCs from global model
AQ initial conditions
UMOS- AQ
Products: - AQHI - Specialized
- Custom
OA
Real time DB
Verif DB
Real time AQ obs
Config, landuse, etc.
AQ assimilation
= Not yet

## Slide 10: RAQDPS: GEM-MACH
GEM-MACH coupled AQ & weather model
Operational environment and systems
Emissions:
- Anthropogenic - Biogenic
- (Forest fires)
AQ piloting from global model
Weather assimilation
Weather BCs from global model
AQ initial conditions
UMOS- AQ
Products: - AQHI - Specialized
- Custom
OA
Real time DB
Verif DB
Real time AQ obs
Config, landuse, etc.
AQ assimilation
= Not yet

## Slide 11: Recent changes to core model
Major upgrade to GEM-MACH AQ model and its GEM core dynamic library
Based on latest weather model GEM v4 (major update).
  New vertical coordinate (hybrid in log-hydrostatic-pressure)
  New vertical discretization (Charney-Phillips staggering) lowest layer depth is now 40-m;
  Physics spin-up capability;
  Global Yin-Yang grid (New LAM grid that align to it);
  New PBL moist TKE scheme
  New orographic blocking scheme
Surface level for tracers now defined at 20m (as opposed to 0m)
Covered this morning in: Recent Upgrades to the Chemical Transport Model Used in the Canadian Operational Regional Air Quality Deterministic Prediction System (Moran et al)

## Slide 12: Recent changes to RAQDPS
Improvements to chemistry modules
  Native (GEM) vertical diffusion scheme for chemical tracers
  Comprehensive mass conservation for tracers, designed for LAM
  Improved below-cloud scavenging
  Corrected problems with emissions, dry deposition
  Gas-phase dry deposition with improved LAI scaling
  New 3D seasonal chemical lateral boundary conditions
  Sea-salt emissions now precede vertical diffusion
  Various minor corrections
Covered this morning in: Recent Upgrades to the Chemical Transport Model Used in the Canadian Operational Regional Air Quality Deterministic Prediction System (Moran et al)

## Slide 13: New RAQDPS domain (Sept 2016) – in green

## Slide 14: RAQDPS: Forest Fires
GEM-MACH coupled AQ & weather model
Operational environment and systems
Emissions:
- Anthropogenic - Biogenic
- (Forest fires)
AQ piloting from global model
Weather assimilation
Weather BCs from global model
AQ initial conditions
UMOS- AQ
Products: - AQHI - Specialized
- Custom
OA
Real time DB
Verif DB
Real time AQ obs
Config, landuse, etc.
AQ assimilation
= Not yet

## Slide 15: FireWork System
FireWork has the same configuration as GEM-MACH, the operational AQ model. The only difference is the inclusion of the near-real-time wildfire emissions
FireWork:
  Run twice daily (initiated at 00 UTC
  and 12 UTC)
  Available at approximately at the same
  time as the operational model
Additional products
  Alternate AQHI based on FireWork
  PM2.5/PM10 maps and animations based on difference fields (FireWork – GEM-MACH) to isolate plumes
  Total column PM2.5/PM10 sums
  Other specialized products available upon request
WildFire Emissions Data
Currently CFFEPS, developed by CWFIS, is being tested and will eventually replace the current FEPS module
See talk from J. Chen et. Al.

## Slide 16: How Important are wildfires for AQ?
"Wildfire in the Pacific Northwest (8776242994)" by Bureau of Land. Licensed under CC BY 2.0 via Wikimedia Commons - https://commons.wikimedia.org/wiki/
2013
2014
Forecasted wildfire emissions contribution to average summertime PM2.5 concentrations
2015
In Canada, the impact of wildfire smoke on air quality is very significant.
Forecasted wildfire emissions contribution to the average summertime PM2.5 concentrations (2013-2015) ranges from a few µg/m3 to over 30µg/m3.
2016

## Slide 17: Considerations for FireWork
Perspective of health partners:
  Forecast: get the timing right
  “Smoke aloft” forecast useful
  Concentrations important for retrospective studies (exposure)
Public forecast
  Probabilistic? “60% chances of heavy smoke” …
  Higher resolution?
    Dispersion may be sufficient for near-source details.
Science gaps
  Plume chemistry: ozone production etc.
  Emissions…
  2-way interactions with weather
Tracer tagging vs assimilation

## Slide 18: Regional Air Quality Deterministic Prediction System (RAQDPS): components
GEM-MACH coupled AQ & weather model
Operational environment and systems
Emissions:
- Anthropogenic - Biogenic
- (Forest fires)
AQ piloting from global model
Weather assimilation
Weather BCs from global model
AQ initial conditions
UMOS- AQ
Products: - AQHI - Specialized
- Custom
OA
Real time DB
Verif DB
Real time AQ obs
Config, landuse, etc.
AQ assimilation
= Not yet

## Slide 19
BIAS
RMSE
O3
Post-processing applied to GEM-MACH raw model output
Reduces model bias and model error at point locations with AQ monitors through through multi-variate linear regression approach
  Applied to meteorological variables since 2000
  Adapted for air quality variables (O3, NO2, PM2.5) in 2010
  Equations are recalculated four times a month
Statistical Model: UMOS-AQ
GEM-MACH
UMOS-AQ
PM2.5
NO2

## Slide 20: RAQDPS: objective analysis
GEM-MACH coupled AQ & weather model
Operational environment and systems
Emissions:
- Anthropogenic - Biogenic
- (Forest fires)
AQ piloting from global model
Weather assimilation
Weather BCs from global model
AQ initial conditions
UMOS- AQ
Products: - AQHI - Specialized
- Custom
OA
Real time DB
Verif DB
Real time AQ obs
Config, landuse, etc.
AQ assimilation
= Not yet

## Slide 21: OA: Objective Analysis for Surface Pollutants
Operational as of February 2013, called RDAQA
Blends model forecasts with surface observations from Canadian regional networks and the U.S. EPA’s AIRNow observation network
  Using an optimal interpolation approach
  Knowledge of the errors of model and observation data is applied to weight each input accordingly
Products available hourly (2x = early and late analyses):
  Available for : PM2.5, O3, NO2, NO, SO2, PM10 and AQHI
A new system is under development (basis for 3D assimilation)
See talk from R. Ménard et al.

## Slide 22: Surface OA increments : winter
O3
PM2.5
NO2
Average of hourly surface analysis increments, January 2016

## Slide 23: Surface OA increments : summer
O3
NO2
PM2.5
Average of hourly surface analysis increments, Julyy 2016

## Slide 24: RAQDPS: verification
GEM-MACH coupled AQ & weather model
Operational environment and systems
Emissions:
- Anthropogenic - Biogenic
- (Forest fires)
AQ piloting from global model
Weather assimilation
Weather BCs from global model
AQ initial conditions
UMOS- AQ
Products: - AQHI - Specialized
- Custom
OA
Real time DB
Verif DB
Real time AQ obs
Config, landuse, etc.
AQ assimilation
= Not yet

## Slide 25: VAQUM: Verification for Air QUality Models
Designed a PostGIS database to store AQ observations and corresponding model outputs
  Can ingest both real time and QC’ed historical datasets
  Allows to produce various statistics & categorical scores
  About 1730 stations (265 CAN, 1465 USA)
  Collecting data since 2007
Essential tool to assess the impact of model updates
Also used to monitor the performance of the operational system
RMSE
MB
NO2
NO2
Automatic Operational Model Evaluation

## Slide 26: VAQUM
Chart: O3 (1,334 stns)
| ECAN | WCAN | EUSA | WUSA
 | 131 | 78 | 819 | 306
Chart: NO2 (283 stns)
| ECAN | WCAN | EUSA | WUSA
 | 84 | 87 | 76 | 36
Chart: PM2.5 (871 stns)
| ECAN | WCAN | EUSA | WUSA
 | 112 | 102 | 406 | 251
Number of stations with available observations within the GEM-MACH domain
PM2.5 stations with 75% observation availability for summer of 2015

## Slide 27: VAQUM Products
Objective Scores – hourly forecasts
Per hour statistics graphs
Per observation value bin graphs
Metropolitan Areas Time Series
Per station statistics
For further details, please see poster number 275 (Monday, 11th January)
Verification Tools for Air Quality Models

## Slide 28: Context: public concern
Years of public outreach raised awareness
As provinces & territories engage in the AQHI program, ECCC adjusting to these partners (e.g. AQHI+)
Media coverage: exposing health risks

## Slide 29: Extending forecast to day 3
Regional weather forecast now providing 84h (exp)
  Can be used as LBCs for the RAQDPS
Indications that skill for day 3 forecast not much weaker than for day 2
Commitment of the AQHI program. Targeting 2018
See poster from Sylvain Ménard et al.

## Slide 30: High resolution
Take advantage of high resolution weather forecast (2.5km)
  Improved BL
  Improved surface temperature
  Capture intra-urban variability
Expected gain in finer representation on emissions
PanAm example:
  Site-specific AQ forecast (as opposed to community average)
See presentation from R. Munoz-Alpizar

## Slide 31: GEM-MACH 2.5km Pollutant Forecast
Summer 2015
Winter 2016
Mean concentration over several stations around Toronto

## Slide 32: Next steps
Major changes to supercomputing environment.
  Development slowed down until mid-2017
  Hope to gain in performance (and delivery times)
RAQDPS
  72h forecasts (next 2y)
  Updated emissions inventories for Canada, U.S. and Mexico (planned for 2017)
  Developing 2.5km subdomains (next 2y)
FireWork
  Improved plume height estimates (2017)
  Improved wildfire emissions estimates (2017)
Products: towards 2D public forecast.
WMS data access (ogc compliant, in beta testing)