## Slide 1: Performance Analysis of the Canadian Operational Statistical Air Quality Post-Processing Package
Radenko Pavlovic
Meteorological Service of Canada
Environment and Climate Change Canada
Authors:
R. Pavlovic1, S. Antonopoulos2, S. Gilbert1, D. Davignon1, A. Teakles3 and M.D. Moran4
1Air Quality Modeling Applications Section, Environment and Climate Change Canada (ECCC), Montreal, Quebec, Canada
2Weather Element Section, ECCC, Montreal, Quebec, Canada
3 Atlantic Air Quality Science Unit, ECCC, Dartmouth, Nova Scotia, Canada
4Air Quality Research Division, ECCC, Toronto, Ontario, Canada
8th IWAQFR 2016, Toronto, Canada

## Slide 2: Statistical Post-Processing (SPP)
Why is SPP important?
  SPP can compensate for models’ inherent systematic errors
  SPP takes into account scales and phenomena not yet resolved by dynamical models
  SPP can be a very helpful tool for operational ECCC AQ forecasters
At the Canadian Meteorological Centre (CMC) Updateable Model Output Statistics (UMOS) is applied as a statistical post-processing system for weather- and AQ-related predictands.

## Slide 3: Statistical Post-Processing (SPP) UMOS
At the CMC, UMOS has been operational since 1995, and UMOS-AQ since July 2010
UMOS-AQ provides station-specific forecasts for PM2.5, NO2, and O3, allowing the calculation of a UMOS-AQ-based AQHI
More information about UMOS-AQ can be found in:
  UMOS-AQ: Forecasting O3, PM25 and NO2 hourly spot concentrations using an Updatable MOS methodology, 2nd IWAQFR, Antonopoulos et al., 2010.
  UMOS-AQ / MIST: Improving O3, PM25 and NO2 GEM-MACH15 surface fields by optimally interpolating Updatable MOS (UMOS) forecasts, NATO-SPS ITM on Air Pollution Modelling and Its Application, Utrecht, The Netherlands, Antonopoulos et al., 2012.

## Slide 4: AQHI Observation Sites vs ECCC Forecast Locations
SCRIBE (Forecast Location)
AQHI Observation Sites
UMOS produces station-specific forecasts
The number of ECCC forecast locations outnumber UMOS-AQ locations

## Slide 5: UMOS-AQ/MIST
MIST
Moteur d'Interpolation STatistique
UMOS-AQ
FORECAST
UMOS-AQ/MIST
SCRIBE
Operational AQ Forecast interface

## Slide 6: UMOS-AQ/MIST and Operational Forecasts
ECCC operational forecasters work directly with UMOS-AQ/MIST; It's the source of the operational AQ interface
If there are potential AQ problems, forecasters will verify AQ observations
If they have some particular concerns, and if time allows, they will analyze direct model outputs
This is why we are focusing on Statistical Post-Packaging Performance

## Slide 7: Canada Averaged Observed and Forecasted PM2.5, NO2 and O3 Concentrations
Summertime – July 2016
Wintertime – January 2016
O3 (ppb)
O3 (ppb)
NO2 (ppb)
NO2 (ppb)
PM2.5 (µg/m3)
PM2.5 (µg/m3)
OBSERVED
RAQDPS
UMOS-AQ/MIST
Significant improvement with UMOS-AQ/MIST
Significant improvement with UMOS-AQ/MIST
Significant improvement with UMOS-AQ/MIST
OBSERVED
RAQDPS
UMOS-AQ/MIST

## Slide 8: Performance Analysis Hourly and Daily Max Objective Scores
Wintertime
Summertime
Daily Max
Hourly
Root Mean Square Error (RMSE) and Correlation Coefficient (R) are also improved with UMOS-AQ/MIST

## Slide 9
Positive differences
WINTERTIME
UMOS-AQ/MIST
Eastern Canada
DIFF=UMOS-AQ/MIST - RAQDPS
Western Canada
DIFF=UMOS-AQ/MIST - RAQDPS
O3
PM2.5
NO2
Negative differences in major cities

## Slide 10
SUMMERTIME
O3
PM2.5
NO2
UMOS-AQ/MIST
Eastern Canada
DIFF=UMOS-AQ/MIST - RAQDPS
Western Canada
DIFF=UMOS-AQ/MIST - RAQDPS
Positive differences
Positive differences
Negative differences in major cities

## Slide 11: Summertime Time Series NO2
Montreal
Vancouver

## Slide 12: Summertime Time Series O3
Calgary
Halifax

## Slide 13: Wintertime Time Series - Toronto
NO2
O3
PM2.5

## Slide 14: UMOS-AQ-MIST‘s Weaknesses (1)
Statistical post-processing (UMOS-AQ/MIST) significantly improves AQ forecasts. However, this system has some weaknesses:
  Smoothing/correcting modelled peak concentrations
  Due to the limited number of AQ stations, UMOS-AQ/MIST correction is applied to a limited area
PM2.5
Toronto

## Slide 15
UMOS-AQ/MIST is not good at handling extreme pollution events, like those generated by wildfires.
  If a source is present for several days, UMOS-AQ starts to adjust the AQ forecasts
Peaks never well represented
UMOS-AQ-MIST‘s Weaknesses (2)
Saskatoon
PM2.5(ug/m3)

## Slide 16: Current and Planned Improvements to Statistical Post-Processing Package (1)
Update post-processing system for extended, 72-hour- long RAQDPS forecast
Adapt Statistical Post-Processing System for wildfire pollution forecasts (FireWork system)
Planned
Ongoing

## Slide 17: Current and Planned Improvements to Statistical Post-Processing Package (2)
New Statistical Post-Processing System named PROGNOS is being developed and tested. This new system is based on the XM-Tool project.
  The XM-Tool initiative is focusing on improving the RAQDPS AQ forecasts in support of the AQHI Forecast Program
  PROGNOS will provide a more versatile and easier to maintain SPP and will be able to process outputs of numerical weather forecast systems
Ongoing
More information about PROGNOS (IWAQFR, Jan 10th):
A. Teakles: PROGNOS - A new MSC initiative to renew the operational statistical post-processing infrastructure
More information about experimental post-processing (IWAQFR, Jan 10th):
A. Teakles: Experimental post-processing of air quality forecasts for the Toronto 2015 PanAm and ParaPanAm Games

## Slide 18: Conclusions (1)
Statistically post-processed (SPP) forecasts are the principal source/tool for ECCC's AQ forecasters
AQ forecasts are significantly improved by SPP when compared to the AQ model's raw outputs. Both hourly and daily max scores (RMSE, MB, R) for NO2, PM2.5 and O3 are improved
SPP has some weaknesses, like forecasting extreme events
Constant improvements are made to the SPP and important system updates are planned for coming years

## Slide 19: Conclusions (2)
POPULATION DENSITY OF CANADA
UMOS-AQ Sites
PM2.5
Useful tool for urban AQ forecasting. In Canada, major urban centres are covered with large number of UMOS-AQ stations.
TORONTO
Source: Statistics Canada, graphic redesign by Geopolitical Futures
Toronto Smog Alert, (CTV News, Toronto, May 9th 2015)

## Slide 20: THANK YOU!